## Slide 1: DSS Overview

## Slide 2: Agenda
What is DSS?
DSS Hardware Overview
  Display Controller
  Video Pipeline
  Write back Pipeline
  Overlay Manager
  Video Port
  Display Interfaces: eDP, DSI, DPI
  DSS Interrupt Architecture
DSS Driver Overview
DSS Advance Features
  Safety Checks
  FIFO Buffer Mapping
  Security Isolation
Display Sharing

## Slide 3: What is DSS?

## Slide 4: Introduction
DSS: Display Sub System
Displays video frames from memory to LCD
Provides the logic to output video frames stored in the memory to the external display interfaces.
Performs multi-layer composition for the display output
Supports a set of industry standard display interfaces to drive wide range of display panel resolutions
Supports Scaling, Color Space Conversion, Blending, Color Keying
4

## Slide 5: DSS Block Diagram for J721E
5

## Slide 6: DSS Hardware Overview

## Slide 7: Display Controller
Four Video Pipelines
  Two Video pipelines - Supporting 8/10-bit/component RGB or 8/10/12-bit/component YUV source data formats with 3/5-tap 16-phase scaler capable of 0.25x to 16x resizing.
  Two Video_Lite pipelines - Supporting 8/10-bit/component RGB or YUV source data formats (including YUV420/422 source data)
Four Overlay Managers
  Fully mapped to all input pipelines
  Multi-layer alpha blending
Four Video Ports
  Support up to four simultaneous 4K display outputs (600MHz pixel clock)
  24/30/36-bit per pixel RGB output
  Additional 8/10-bit per component YUV422 embedded sync stream (BT1120/BT656) on every output
One optional Write-back pipeline with a scaler to perform memory to memory operations or to capture one of the display outputs.
DMA controller capable of supporting up to 8K-wide input source frame
7

## Slide 8: Display Controller Architecture
8

## Slide 9: Video/Video Lite Pipeline
The video pipeline is connected to the video DMA buffer controller for the input port and to the overlay manager. It performs all functionalities of a Graphics pipeline.
  Polyphase-filter based resizer
  Programmable BCHS (Brightness/Contrast/Hue/Saturation) control
  Luma-key support (for Blue-Ray application)
  Crop support at the output of the video pipeline
Video Lite is identical to the Video pipeline except polyphase-filter based resizer is not included
9

## Slide 10: Write back Pipeline
The write-back pipeline is connected to
  a pipeline output (video lite 2 pipeline only for J721E)
  the output of one of the overlay manager, either in M2M (memory-to-memory) or Capture mode.
Write back pipeline consists of
  Color Space Conversion Unit
  Resizer unit
  RGB truncation logic
10

## Slide 11: Overlay Manager
Composites selected input layers together to generate the final display output frame based on
  Priority rule following the display Z-order (selected by configuring the input selector)
  Color key configurations (destination and source transparency)
  Alpha Blending values (using the Alpha component of each pixel or a global alpha value set by the user)
  Size and position attributes of the source window data
Each overlay manager supports a simple internal color bar insertion to enable testing of display output interface without using the frame buffer data from the memory
11

## Slide 12: Video Port
36-bit per pixel on the RGB output interface (12-bits per component)
Independent programmable timing generators for each display output to support – up to 600 MHz pixel clock video formats
Fully programmable Color Space Conversion matrix to serve as color phase rotation (CPR) and/or as Brightness/Contrast/Saturation control on the combined output
Selection between RGB(progressive) and YUV422(progressive/interlaced) output pixel format. YUV4:2:2 only available when BT656/1120 output is enabled.
12

## Slide 13: Display Interfaces
J721E supports below display interfaces:
  One Display Port/embedded Display Port (DP/eDP)
  One MIPI Display Serial Interface (DSI) port
  Two Display Parallel Interface (DPI) ports.
Future devices will have multiple DP/eDP and DSI ports
The DP/eDP interface supports the following features:
  VESA Display Port (DP) 1.3 specification compliant with DSC(1.1)/FEC support
  VESA embedded Display Port (eDP) 1.4 specification compliant
  Physical link rates up to HBR3 (up to 8.1 Gbps per lane)
  Video pixel clock rate range from 25-600MHz
DSI interface supports following features:
  4,2, or 1 data lane configurations
  MIPI Display Serial Interface (DSI) 1.3 specification compliant with DSC(1.1) support
  D-PHY 1.2 Physical link rates up to 2.5 Gbps per lane
  Video pixel clock rate range from 25-400MHz (up to 3K Display Panels)
  4,3,2, or 1 data lane configurations
13

## Slide 14: Connectivity Diagram for J721E
14

## Slide 15: DSS Interrupt Architecture
DSS supports multiple interrupt outputs each of which can be set independently
There are separate interrupt lines for different category of events:
  Functional
  Safety
  Security
There are four common register regions which allows fully independent monitoring/control of the interrupt events by multiple hosts
15

## Slide 16: DSS Driver Overview
16

## Slide 17: FVID2 Introduction
What is FVID2?
  Provides interface to streaming operations like queuing of buffers to driver and getting back a buffer from the driver
  Abstracts the underlying hardware for the video application with a standard set of interface
  Gives a same look and feel for video applications across different SOC
  Interface is independent of OS/Hardware/Driver
  FVID2 is currently supported on BIOS
What is not FVID2?
  Not the actual driver
  Does not define hardware specific APIs and structures
FVID2 Interfaces
  Fvid2_init, Fvid2_deInit
  Fvid2_create, Fvid2_delete
  Fvid2_start, Fvid2_stop
  Fvid2_queue, Fvid2_dequeue
  Fvid2_processFrames, Fvid2_getProcessedFrames
  Fvid2_control
17

## Slide 18: Typical Application Flow
18

## Slide 19: Directory Structure
DSS CSL RL and CSL FL files are present in <pdk>/packages/ti/csl/src/ip/dss
FVID2 driver is present in <pdk>/packages/ti/drv/fvid2
DSS driver is present in <pdk>/packages/ti/drv/dss
19

## Slide 20: DSS Advance Features

## Slide 21: DSS Safety Checks
21

## Slide 22: FIFO Buffer Mapping (1/2)
When Scaler is enabled, the DMA needs to send multiple lines simultaneously (in parallel) to the VID pipeline.
The number of lines could be up to 4 lines in parallel (the case when there is downscaling by 4).
The buffer in this case needs to be used in “ping-pong” mode.
Hence, the requirement on the buffer memory size is to have space to store at least eight full lines (The size in bytes of a line depends on the resolution as well as the pixel format)
The below table lists the size of a line in bytes for the common resolutions and formats
22
Resolution | Format | 1-line (in KB) | 8-lines (in KB)
1920 (1080p) | ARGB32 (32bpp) | 7.5 | 60
 | RGB24p (24bpp) | 5.625 | 45
 | YUV422 (16bpp) | 3.75 | 30
2560 (2.5K) | ARGB32 (32bpp) | 10 | 80
 | RGB24p (24bpp) | 7.5 | 60
 | YUV422 (16bpp) | 5 | 40
4096 (4K) | ARGB32 (32bpp) | 16 | 128
 | RGB24p (24bpp) | 12 | 96
 | YUV422 (16bpp) | 8 | 64

## Slide 23: FIFO Buffer Mapping (2/2)
Each channel in DMA is allocated a uniform buffer size of 64 Kilo Bytes at reset.
To support resolutions larger than 4K YUV or 2K ARGB (with ping-pong configuration), the default buffer size of 64KB per RD channel is not sufficient as demonstrated above.
In such cases, the design allows dynamic repartition of the allocated buffers across the different RD channels. In this way each RD channel can have a variable buffer size allocated to it, starting from a minimum of 16KB to a maximum of 256KB, in 16KB increments.
23

## Slide 24: Security Isolation
Configuration Firewall – Each Common Region, Pipe, Overlay & Video Port has 64KB FW region
Secure Mode setting – Hardware based connection check/illegal connection prevention
Multiple sets of Interrupt Logic for secure/non-secure host handling
24

## Slide 25: Display Sharing

## Slide 26: Display Sharing for K3 SoCs
Cockpit Use case: Simultaneous Safety and QM Requirements on Display
  Safety content is generated by a safety certified OS running on a dedicated core
  QM content is usually generated by HLoS (Linux)
  There may be multiple instances of QM SW running on different cores / same core with virtualization support
Static partitioning of Resources
  Resources are allocated at system boot time
VP thread as Atomic Resource Partition Entity
  VP Thread : A VP, Overlay-Manager and all pipes terminating at the VP
  Any core can drive one / multiple end-to-end VP threads
  All pipe, overlay manager and VP register updates for a thread shadowed by asserting VPx.GO bit
  All interrupts for pipes and VP in a thread used by the driving core
Distributed DSS Initialization
  R5F boots up first and initializes DSS
  Any core who owns a VP thread initializes the thread specific setup
  Pipes are initialized and setup on-demand
Pipe Subscription and IPC based Frame update requests
  VP thread owner can
    Reserve a set of pipes to be used by local applications
    Export a set of pipes to a remote core via a local display-server
  Remote cores probe a display-server to get a list of exported pipes
  Remote cores send frame update requests to display-server for exported pipes
26

## Slide 27: Design: Logical HW Split
27

## Slide 28: Thank You!
28